TightVNC Extensions to the RFB Protocol
Author: Constantin Kaplinsky, TightVNC Group
# Protocol messages (server to client)

# Protocol messages (client to server)
VideoRectangleSelection
Type	Code	Name Signature	Vendor Signature
client to server message	151	"VRECTSEL"	"TGHT"

This message instructs the server to treat the specified part of the framebuffer as video data. The server can use this information as a hint for more efficient update tracking and encoding. For example, the server might assume that the corresponding pixels would be continuously changing (no polling necessary) and can be efficiently encoded with JPEG.
Data formats:
Length, bytes	Type	Description
1	U8	message-type = 151
1	U8	reserved = 0
2	U16	x
2	U16	y
2	U16	width
2	U16	height

Each new VideoRectangleSelection message discards previous selection of video rectangle. If either width or height is set to zero, it discards video area selection completely, so the server would consider video area selection undefined.
Width must be a multiple of 16, height must be a multiple of 8. This limitation is imposed by specific JPEG encoders that potentially can be used by TightVNC servers. The values of x and y can be arbitrary, but the complete rectangle should reside within the framebuffer bounds. However, if the client sends values not conforming to these requirements, the server should not fail, it should correct the values appropriately.